## Slide 1
MONTHLY REPORT
Vulkan Persistent Thread WorkGraph POC
May 2026 optimization evaluation: validating global atomic traffic as the queue bottleneck
30.75 ms
Baseline median
clean compute_ms
0.99 ms
Final median
main integrated
31.0x
Median speedup
same workload
Adopted path: Q1/Q2 queue sharding + Q1 lane-pop. Request batching is tested, documented, and not adopted for the current protocol/workload.
AMD RX 7900 XTX / RDNA 3

## Slide 2
Vulkan Persistent Thread WorkGraph POC
Executive summary: hypothesis to validated bottleneck
02
2026-05-25
Optimization Evaluation v2
HYPOTHESIS
Hypothesis
The persistent-thread queue architecture is atomic-heavy, so global atomic traffic was suspected.
EVIDENCE
Evidence
Clean timing plus counter-enabled runs identify queue contention, CAS failures, backlog, and ready-spin behavior.
ADOPTED PATH
Adopted path
Q1 sharding, Q2 sharding, and Q1 lane-pop reduce shared atomic hotspots.
RESULT
Result
Median clean compute drops from 30.75 ms to about 0.99 ms on the final integrated path.
Performance results come from clean timestamp runs; atomic counters are used to explain the bottleneck behavior.

## Slide 3
Vulkan Persistent Thread WorkGraph POC
Recap architecture: persistent workers and atomic queues
03
2026-05-25
Optimization Evaluation v2
Node A
Seed edges once
Q1
atomic count/head/tail ready flag
Node B
Subdivide work
Q2
atomic count/head/tail ready flag
Node C
Write vertices
VB Render
Deterministic draw
Why atomic traffic is plausible
- Cross-workgroup handoff uses atomics for correctness on RDNA 3.
- Queue state and ready flags are shared by many lanes and workgroups.
What v2 validates
- Metrics confirm queue contention instead of treating it as an assumption.
- Optimizations that split or diversify queue access dominate the gains.

## Slide 4
Vulkan Persistent Thread WorkGraph POC
Prior hypothesis: suspected, not yet proven
04
2026-05-25
Optimization Evaluation v2
PRIOR REPORT
Known state
- Correctness-first POC was working.
- The architecture depended heavily on atomics.
- Performance investigation was not complete.
THIS REPORT
Validation goal
- Build metrics that explain atomic behavior.
- Use controlled experiments to test the bottleneck hypothesis.
- Only adopt changes that improve clean timestamp runs.
This report turns the atomic-traffic hypothesis into an evidence-backed bottleneck diagnosis.

## Slide 5
Vulkan Persistent Thread WorkGraph POC
Measurement framework: separate timing from structure
05
2026-05-25
Optimization Evaluation v2
Run type | Purpose | Primary readout | What it supports
Clean timestamp runs | Performance result | Median compute_ms after warmup | Duration and speedup
Counter-enabled runs | Bottleneck diagnosis | CAS fail ratio, backlog, ready-spin, empty-pop | Queue contention behavior
RGP occupancy | Profiler context | Wavefront view and event timing | Tool interpretation boundary
Timing
Clean timestamp runs quantify performance.
Counters
Atomic counters explain queue pressure.
Profiler
RGP provides context, not standalone proof.
This separation keeps duration numbers comparable while still exposing why each optimization changed the queue behavior.

## Slide 6
Vulkan Persistent Thread WorkGraph POC
Atomic metrics interpretation
06
2026-05-25
Optimization Evaluation v2
Metric | Interpretation | Decision use
CAS fail per success | Many lanes or workgroups retry the same queue state. | High contention; sharding should reduce this.
Attempts vs success | Control path does repeated work without throughput. | Detects wasted polling.
Queue high-water | Producer/consumer balance and backlog. | Shows B/C balance and Q2 pressure.
Ready-spin / empty-pop | Consumers claimed or probed before useful work was ready. | Explains request batching regressions.
Clean vs counter runs | Timing and diagnosis are collected separately. | Keeps performance and cause analysis comparable.
The bottleneck diagnosis is strongest when clean duration and atomic metrics move in the same direction.

## Slide 7
Vulkan Persistent Thread WorkGraph POC
Bottleneck timeline: median clean compute_ms
07
2026-05-25
Optimization Evaluation v2
Stage | Config | Median ms
Baseline | Q1 batch on, Q2 scalar, C=24/B=72 | 30.7499
B/C ratio | C=40/B=56 | 27.8938
Q1 sharding | Q1s16/Q2s1, C=38/B=58 | 13.7416
Q2 sharding | Q1s16/Q2s16, C=16/B=80 | 5.5708
Q1 lane-pop | Q1s16/Q2s16, C=24/B=72 | 3.8509
High shard scaling | Q1s256/Q2s256, C=24/B=72 | 0.9868
Every major improvement corresponds to reducing or distributing queue atomic contention.

## Slide 8
Vulkan Persistent Thread WorkGraph POC
Optimization 1: B/C ratio
08
2026-05-25
Optimization Evaluation v2
C/B | Median ms | Avg ms
24/72 | 30.7499 | 30.3533
32/64 | 28.5262 | 28.4431
40/56 | 27.8938 | 27.9742
48/48 | 28.5412 | 28.5873
64/32 | 30.2860 | 30.2509
EVIDENCE
What this stage proved
- Increasing Node C writers reduced Q2 backlog.
- C=40/B=56 improved median compute, but queue contention remained the larger bottleneck.
50k -> 9k
Q2 high-water trend
counter-enabled runs
30.75 -> 27.89
Median ms
clean runs
Interpretation: writer balance matters, but it does not remove the single hot queue state.

## Slide 9
Vulkan Persistent Thread WorkGraph POC
Optimization 2: Q1 sharding
09
2026-05-25
Optimization Evaluation v2
Q1 shards | C/B | Median ms | Avg ms
4 | 40/56 | 23.3164 | 23.2366
8 | 40/56 | 17.9518 | 17.9043
16 | 36/60 | 13.9788 | 13.9523
16 | 38/58 | 13.7416 | 13.7046
16 | 40/56 | 14.1297 | 14.084
Before
Single Q1 queue hot count/head/tail
After
Q1 split across shards same queue protocol
- Q1 sharding turns one global atomic hotspot into multiple smaller hotspots.
- After Q1 pressure drops, Q2 queue pressure becomes the next clear bottleneck.
13.74 ms
Q1s16/Q2s1 median
The improvement stacks with B/C tuning, which supports the contention hypothesis.

## Slide 10
Vulkan Persistent Thread WorkGraph POC
Optimization 3: Q2 sharding
10
2026-05-25
Optimization Evaluation v2
Q2 shards | Median ms | Avg ms | Speedup
1 | 16.9962 | 16.9529 | 1
2 | 10.2455 | 10.2431 | 1.655
4 | 8.3799 | 8.3824 | 2.022
8 | 6.8738 | 6.8656 | 2.469
16 | 6.0924 | 6.0839 | 2.787
READOUT
Second major structural optimization
- Q1 sharding exposed Q2 count/head/tail as the next global pressure point.
- Q2 sharding lowered median compute to about 5.57 ms after B/C rebalance.
5.57 ms
Q1s16/Q2s16 median
2.79x
vs Q2s1 in sweep
The repeated pattern is not general compute optimization. It is queue hotspot removal.

## Slide 11
Vulkan Persistent Thread WorkGraph POC
Optimization 4: Q1 lane-pop
11
2026-05-25
Optimization Evaluation v2
Mode | Median ms | Avg ms | Min ms
lane-pop off, C=16/B=80 | 5.60 | 6.01 | 5.54
lane-pop on, C=16/B=80 | 4.00 | 4.39 | 3.90
lane-pop on, C=24/B=72 | 3.8509 | 3.8526 | 3.7292
Scan-start change
Old: wgId % Q1_QUEUE_SHARDS
New: (wgId * local_size_x + localId) % Q1_QUEUE_SHARDS
This is not request batching. It keeps the queue protocol but diversifies where lanes begin scanning, reducing avoidable local shard contention.

## Slide 12
Vulkan Persistent Thread WorkGraph POC
Optimization 5: high shard scaling
12
2026-05-25
Optimization Evaluation v2
Q1/Q2 | Median | P90
16 | 3.8509 | 3.8998
32 | 2.4002 | 2.4205
64 | 1.5427 | 1.5572
128 | 1.1372 | 1.1545
192 | 1.0808 | 1.0969
256 | 0.9868 | 1.0068
384 | 1.0478 | 1.0688
512 | 1.1178 | 1.1342
256 / 256
Adopted default
256 shards is the effective range in this architecture. Higher counts begin losing benefit to probing and indexing overhead.

## Slide 13
Vulkan Persistent Thread WorkGraph POC
Request batching: why the idea was plausible
13
2026-05-25
Optimization Evaluation v2
Problem
Per-item dequeue CAS creates heavy retry traffic
Idea
One subgroup claim reserves multiple slots
Expected
Fewer CAS attempts per consumed item
Risk
More ready-spin or empty slots
Validation question
Does request batching improve clean median and P90 in the same controlled suite, or does it only move the cost into ready-spin and wasted polling?

## Slide 14
Vulkan Persistent Thread WorkGraph POC
Request batching controlled results
14
2026-05-25
Optimization Evaluation v2
Default 256 suite | Samples | Median | P90
off | 354 | 1.9432 | 1.9691
l8 | 354 | 11.7109 | 11.7553
l16 | 354 | 11.4284 | 11.4658
l32 | 354 | 11.2778 | 11.3034
l1 | 0 | no samples | no samples
l2 | 0 | no samples | no samples
l4 | 0 | no samples | no samples
Stress 16 suite | Median | P90
off | 4.2442 | 4.9059
l4 | 4.2553 | 4.6734
l8 | 4.1737 | 5.1022
l16 | 4.2623 | 5.3898
l32 | 4.1165 | 5.2635
1.9432 ms
Suite-local off baseline
11 ms range
Default 256 batching regression
Conclusion: batching can help selected stress medians, but it does not generalize and can severely regress the default 256-shard setup.

## Slide 15
Vulkan Persistent Thread WorkGraph POC
Adopted default: current main path
15
2026-05-25
Optimization Evaluation v2
256
Q1 shards
256
Q2 shards
ON
Q1 lane-pop
24 / 72
C/B workers
Setting | Value
MAX_QUEUE_SHARDS | 256
Q1_QUEUE_SHARDS_DEFAULT | 256
Q2_QUEUE_SHARDS_DEFAULT | 256
ENABLE_Q1_LANE_POP | default on
NODE_C_START | 72, so C=24/B=72
The main path is not a magic parameter. It is the endpoint of a sequence that repeatedly removed queue/global atomic contention.

## Slide 16
Vulkan Persistent Thread WorkGraph POC
Final confirmation: main integrated repeats
16
2026-05-25
Optimization Evaluation v2
Run | Samples | Median | P10 | P90 | Min
repeat 1 | 1836 | 0.9904 | 0.9804 | 1.0036 | 0.9659
repeat 2 | 1867 | 0.9916 | 0.9819 | 1.0053 | 0.9657
repeat 3 | 1868 | 0.9907 | 0.9810 | 1.0042 | 0.9593
repeat 4 | 1866 | 0.9903 | 0.9807 | 1.0038 | 0.9615
~0.99 ms
Median band across repeats
~1.00 ms
P90 band across repeats
Repeat runs show a stable median near 0.99 ms with P90 close to 1.00 ms.

## Slide 17
Vulkan Persistent Thread WorkGraph POC
Key conclusion
17
2026-05-25
Optimization Evaluation v2
Verified
Atomic traffic was validated as the bottleneck class.
Adopted
Sharding plus lane-pop is the main optimization path.
Rejected
Request batching is not adopted for this protocol/workload.
The current architecture can reach about 0.99 ms median, but the remaining design question is whether work can stay more local before spilling to global queues.

## Slide 18
Vulkan Persistent Thread WorkGraph POC
Next plan: wave-local work retention
18
2026-05-25
Optimization Evaluation v2
Current baseline
Global sharded queues Q1/Q2 = 256/256
Prototype
Wave-local retention spill-to-global fallback
Compare
global atomic count spill ratio tail stability
- Keep 256-shard main path as the baseline.
- Measure global atomic count, wave-local handoff count, spill-to-global ratio, and compute duration.
- Revisit request batching only if the queue protocol changes.
- Keep timing and atomic-counter diagnosis separate in the next experiment.

## Slide 19
Vulkan Persistent Thread WorkGraph POC
Appendix: code snippets
19
2026-05-25
Optimization Evaluation v2
SHARD PUSH
Shard push / ready publish
uint shard = mixHash(h) % Q1_QUEUE_SHARDS; if (atomicCompSwap(control.q1[shard].count, cur, cur + 1u) == cur) { uint localSlot = atomicAdd(control.q1[shard].tail, 1u) % capacity; atomicExchange(queue1.tasks[slot].payload[5], 1u); }
Q1 LANE-POP
Q1 lane-pop start shard
uint worker = wgId * local_size_x + localId; uint homeShard = (ENABLE_Q1_LANE_POP != 0u) ? (worker % Q1_QUEUE_SHARDS) : (wgId % Q1_QUEUE_SHARDS);
Q2 BATCH CAS
Request batching CAS claim
uint claim = min(available, Q2_DEQUEUE_BATCH_LIMIT); if (atomicCompSwap(control.q2[shard].count, cur, cur - claim) == cur) { baseHead = atomicAdd(control.q2[shard].head, claim); }

## Slide 20
Vulkan Persistent Thread WorkGraph POC
Appendix: numeric source files
20
2026-05-25
Optimization Evaluation v2
Artifact | Path
Normalized measurements | reports/2026-05/metrics/monthly_v2_normalized_measurements_20260525.csv
Measurement notes | reports/2026-05/metrics/monthly_v2_measurement_notes_20260525.md
Main backbone | reports/2026-05/metrics/q2_shards_20260510/research_backbone_20260510.md
Request batching summary | reports/2026-05/metrics/request_batching_validation_20260525/request_batching_validation_summary.csv
Primary performance numbers are sourced from the normalized measurement table.