## Slide 1
Vulkan Persistent Thread
Producer-Consumer Network POC
Monthly Progress Report
2026 / 04
LUO-WEN-CHIEN
AMD RX 7900 XTX | RDNA 3 | Vulkan 1.4
1 / 8

## Slide 2
Research Goal & Motivation
Goal
Implement a D3D12 Work Graph analogue on Vulkan using persistent compute shaders
Why
Find key considerations during design
Measure scheduling overhead & on-chip memory utilization
Target: AMD RX 7900 XTX (RDNA 3, 96 CUs, 24GB VRAM)
Test Case
Koch Snowflake fractal generation + real-time rendering
Recursive branching workload: 1 edge → 4 sub-edges per level
2 / 8

## Slide 3
System Architecture
HOST (CPU)
▼
Node A
(Seed)
▶
Q1
▶
Node B
(Subdivide)
↺ feedback (depth < MAX)
▶
Q2
▶
Node C
(Write VB)
▼
Vertex Buffer
(SSBO + VB)
Per-Frame Command Buffer Flow:
// buildCommandBuffers() - per frame
vkCmdFillBuffer(cmd, controlBuf, ...); // 1. GPU Reset
vkCmdFillBuffer(cmd, q1Buf/q2Buf, ...);
vkCmdPipelineBarrier(...TRANSFER → COMPUTE); // 2. Barrier
vkCmdDispatch(cmd, 96, 1, 1); // 3. Compute (3072 threads)
vkCmdPipelineBarrier(...COMPUTE → VERTEX);// 4. Barrier
vkCmdDraw(cmd, 24576, 1, 0, 0); // 5. Render
3 / 8
Graphics Pipeline
→ Display
◀

## Slide 4
Persistent Thread Model
Workgroup | Role | Queue | Action
WG 0 | Node A + B | Seed → Q1 | Thread 0 seeds 3 edges, then all do Node B
WG 1–71 | Node B | Q1 → Q1 / Q2 | Pop Q1, subdivide, push back Q1 or forward Q2
WG 72–95 | Node C | Q2 → VB | Pop Q2, write vertices, count → stopFlag
Single dispatch: vkCmdDispatch(96, 1, 1) = 96 WG × 32 threads = 3,072 persistent threads
Shader Main Loop Structure:
void main() {
uint wgId = gl_WorkGroupID.x;
uint localId = gl_LocalInvocationID.x;
// Node A: WG 0, Thread 0 seeds 3 edges (once)
if (wgId == 0 && localId == 0) {
if (atomicCompSwap(control.seedDone, 0, 1) == 0)
pushQ1(edge_AB); pushQ1(edge_BC); pushQ1(edge_CA);
}
barrier(); memoryBarrierBuffer();
// Main persistent loop
while (control.stopFlag == 0) {
if (wgId < NODE_C_START) { /* Node B */ }
else { /* Node C */ }
}
}
4 / 8

## Slide 5
Atomic Queue Mechanism
Ring Buffer Structure
QueueControl: head / tail / count
Task: payload[6] (4×float + depth + ready)
Push Protocol:
1. CAS count (reserve slot)
2. atomicAdd tail (get slot index)
3. Write payload[0–4]
4. memoryBarrierBuffer()
5. atomicExchange(ready, 1)
Pop Protocol:
1. CAS count (claim item)
2. atomicAdd head (get slot)
3. Spin: atomicCompSwap(ready,1,0)
4. Read payload
pushQ1() Implementation:
bool pushQ1(uint p0, uint p1, uint p2,
uint p3, uint p4) {
while (control.stopFlag == 0) {
uint cur = control.q1.count;
if (cur < QUEUE_SIZE) {
// CAS: reserve a slot
if (atomicCompSwap(control.q1.count,
cur, cur+1) == cur) {
uint slot = atomicAdd(
control.q1.tail, 1) % QUEUE_SIZE;
// Write payload
queue1.tasks[slot].payload[0] = p0;
queue1.tasks[slot].payload[1] = p1;
queue1.tasks[slot].payload[2] = p2;
queue1.tasks[slot].payload[3] = p3;
queue1.tasks[slot].payload[4] = p4;
memoryBarrierBuffer();
// Signal ready (atomic!)
atomicExchange(
queue1.tasks[slot].payload[5], 1u);
return true;
}
}
}
return false;
}
5 / 8

## Slide 6
Cross-Workgroup Memory Sync
Bug 1
Missing coherent modifier
Node C read stale count from L0/L1 cache → no task consumption
Fix: Added coherent to all SSBO declarations
Bug 2
Producer-consumer data race
Producer increments count then writes data; consumer reads uninitialized
Fix: Added per-slot payload[5] ready flag protocol
Bug 3
Plain store cross-CU unreliable
Plain store of ready flag not visible across CUs
Fix: All ready flags use atomicExchange / atomicCompSwap
Memory Visibility:
Method | Same WF | Same CU | Cross-CU
Plain load/store | ✔ | ~ | ✘
coherent | ✔ | ✔ | ~
Atomic (CAS/Exch) | ✔ | ✔ | ✔
6 / 8

## Slide 7
Koch Snowflake Algorithm
Subdivision Rule:
Each edge P1→P2 splits into 4 sub-edges:
P1 → A → C → B → P2
A, B = 1/3, 2/3 points along P1P2
C = apex point, rotated +60° from A
Growth: 3 × 4^depth edges
depth=4: 768 edges (1,536 vertices)
depth=6: 12,288 edges (24,576 vertices)
Node B: Subdivision Core:
// Koch subdivision: 1 edge -> 4 sub-edges
float dx = (x2 - x1) / 3.0;
float dy = (y2 - y1) / 3.0;
// A = 1/3 point, B = 2/3 point
float kax = x1 + dx, kay = y1 + dy;
float kbx = x1 + 2*dx, kby = y1 + 2*dy;
// C = apex (rotate +60° from A)
float cos60 = 0.5;
float sin60 = 0.8660254037844387;
float kcx = kax + dx*cos60 - dy*sin60;
float kcy = kay + dx*sin60 + dy*cos60;
// Push 4 sub-edges (depth+1)
pushQ1(P1→A); pushQ1(A→C);
pushQ1(C→B); pushQ1(B→P2);
GPU Self-Termination:
// Node C: auto-shutdown when all edges processed
uint processed = atomicAdd(control.totalProcessed, 1) + 1;
if (processed >= MAX_DEPTH_EDGES) {
atomicExchange(control.stopFlag, 1u); // all threads exit
}
Current Config (depth=6)
12,288 edges
24,576 vertices
7 / 8

## Slide 8
Progress & Next Steps
Completed
✔ Phase 1-2
Persistent threading, CAS-based queue, CPU monitoring
✔ Phase 3
Node A→B→C pipeline, feedback loop, workgroup roles
✔ Phase 4.1
GPU self-termination, per-frame compute+render, windowed display
Key Achievements:
• Cross-CU atomic sync validated on RDNA 3
• Zero CPU intervention (GPU self-scheduling)
• Single dispatch replaces multi-pass pipeline
• Koch snowflake: deterministic output verified
Next: Phase 4.2
GPU Timestamp Queries
vkCmdWriteTimestamp for compute timing measurement
CAS Failure Counters
Quantify atomic contention & scheduling overhead
LDS Queues
Intra-workgroup shared memory (10-100× latency reduction)
Subgroup Optimization
ballot/shuffle for RDNA3 occupancy tuning
8 / 8

## Slide 9
Per-frame pipeline
Current design is reproducible and profiler-friendly, but compute and graphics are serialized.
workgraph_poc.cpp:267-322
vkCmdFillBuffer(cmd, compute.controlBuf, ...); vkCmdFillBuffer(cmd, compute.q1Buf, ...); vkCmdFillBuffer(cmd, compute.q2Buf, ...); vkCmdPipelineBarrier(... TRANSFER -> COMPUTE ...); vkCmdDispatch(cmd, NUM_WORKGROUPS, 1, 1); vkCmdPipelineBarrier(... COMPUTE -> VERTEX_INPUT ...); vkCmdDraw(cmd, EXPECTED_VERTICES, 1, 0, 0);
What it does
Each frame runs reset, compute, synchronization, then render in a single ordered command-buffer path.
Risk
This is a good baseline, but it does not expose async compute / graphics overlap potential.
Possible fix
Keep this baseline for correctness; later evaluate separate compute/gfx queues or finer scheduling boundaries.
9 / 14

## Slide 10
GPU-side termination
The shader stops itself based on a completed-edge counter.
headless.comp:153-160
uint base = atomicAdd(control.vertexCount, 2); output_vb.vertices[base] = vec2(x1, y1); output_vb.vertices[base + 1] = vec2(x2, y2); uint processed = atomicAdd(control.totalProcessed, 1) + 1; if (processed >= MAX_DEPTH_EDGES) { atomicExchange(control.stopFlag, 1u); }
What it does
Node C owns completion: every written edge increments totalProcessed and may raise stopFlag.
Risk
The stop condition is count-only. If MAX_DEPTH_EDGES or workload shape changes incorrectly, it can stop early or spin longer than needed.
Possible fix
Add a second condition such as queue drain / in-flight accounting while preserving GPU-side termination.
10 / 14

## Slide 11
Static role mapping
Workgroup ID decides whether a worker subdivides or writes output.
workgraph_poc.cpp:10-11, headless.comp:92-138
#define NUM_WORKGROUPS 96 #define NODE_C_START 72 while (control.stopFlag == 0) { if (wgId < NODE_C_START) { // NODE B: Subdivider } else { // NODE C: Writer } }
What it does
The current split is static: 72 workgroups for Node B and 24 workgroups for Node C.
Risk
A fixed B/C ratio can become imbalanced when queue pressure changes, increasing wait time on one side.
Possible fix
Treat NODE_C_START as a tuning knob first; later consider role switching based on queue pressure.
11 / 14

## Slide 12
Fixed-size backing queues
Queue capacity is a correctness and progress concern, not only a memory-size choice.
workgraph_poc.cpp:8, headless.comp:29-45
#define QUEUE_SIZE 16384 bool pushQ1(...) { while (control.stopFlag == 0) { uint cur = control.q1.count; if (cur < QUEUE_SIZE) { if (atomicCompSwap(control.q1.count, cur, cur + 1) == cur) { uint slot = atomicAdd(control.q1.tail, 1) % QUEUE_SIZE; ... } } } }
What it does
Producer threads reserve queue slots using count CAS and tail atomic increments.
Risk
If the queue is full, producers keep retrying. Too small increases waiting; too large increases footprint and locality pressure.
Possible fix
Define queue sizing from worst-case frontier growth plus margin; later add queue-pressure counters.
12 / 14

## Slide 13
Atomic queue handoff
Correctness depends on a per-slot ready flag protocol.
headless.comp:33-41, 97-101
// Producer atomicCompSwap(control.q1.count, cur, cur + 1); uint slot = atomicAdd(control.q1.tail, 1) % QUEUE_SIZE; queue1.tasks[slot].payload[0] = p0; ... memoryBarrierBuffer(); atomicExchange(queue1.tasks[slot].payload[5], 1u); // Consumer while (atomicCompSwap(queue1.tasks[slot].payload[5], 1u, 0u) != 1u) { ... }
What it does
The payload is written first; only then does the producer publish the slot with payload[5].
Risk
This protects cross-CU visibility, but global counters and ready flags can become contention hotspots.
Possible fix
Reduce global atomic pressure with batching, per-workgroup staging, or LDS/local queues.
13 / 14

## Slide 14
Spin wait risk
The risk is identified, but spin-cost measurement is not part of this report.
headless.comp:99-101, 143-145
// Q1 consumer waits for producer publish while (atomicCompSwap(queue1.tasks[slot].payload[5], 1u, 0u) != 1u) { if (control.stopFlag != 0u) return; } // Q2 uses the same ready-flag spin protocol while (atomicCompSwap(queue2.tasks[slot].payload[5], 1u, 0u) != 1u) { if (control.stopFlag != 0u) return; }
What it does
Consumers may busy-spin until the reserved queue slot becomes visible and ready.
Risk
Under producer-consumer imbalance, retries can grow and reduce effective throughput before arithmetic becomes the bottleneck.
Possible fix
Do not claim measured cost yet. Later evaluate backoff, role switching, and shorter handoff windows.
14 / 14