## Slide 1
Vulkan Persistent Thread
Producer-Consumer Network POC
Monthly Progress Report
2026 / 04
LUO-WEN-CHIEN
AMD RX 7900 XTX | RDNA 3 | Vulkan 1.4
1 / 8

## Slide 2
Research Goal & Motivation
Goal
Implement a D3D12 Work Graph analogue on Vulkan using persistent compute shaders
Why
Find key considerations during design
Measure scheduling overhead & on-chip memory utilization
Target: AMD RX 7900 XTX (RDNA 3, 96 CUs, 24GB VRAM)
Test Case
Koch Snowflake fractal generation + real-time rendering
Recursive branching workload: 1 edge → 4 sub-edges per level
2 / 8

## Slide 3
System Architecture
HOST (CPU)
▼
Node A
(Seed)
▶
Q1
▶
Node B
(Subdivide)
↺ feedback (depth < MAX)
▶
Q2
▶
Node C
(Write VB)
▼
Vertex Buffer
(SSBO + VB)
Per-Frame Command Buffer Flow:
// buildCommandBuffers() - per frame
vkCmdFillBuffer(cmd, controlBuf, ...); // 1. GPU Reset
vkCmdFillBuffer(cmd, q1Buf/q2Buf, ...);
vkCmdPipelineBarrier(...TRANSFER → COMPUTE); // 2. Barrier
vkCmdDispatch(cmd, 96, 1, 1); // 3. Compute (3072 threads)
vkCmdPipelineBarrier(...COMPUTE → VERTEX);// 4. Barrier
vkCmdDraw(cmd, 24576, 1, 0, 0); // 5. Render
3 / 8
Graphics Pipeline
→ Display
◀

## Slide 4
Persistent Thread Model
Workgroup | Role | Queue | Action
WG 0 | Node A + B | Seed → Q1 | Thread 0 seeds 3 edges, then all do Node B
WG 1–71 | Node B | Q1 → Q1 / Q2 | Pop Q1, subdivide, push back Q1 or forward Q2
WG 72–95 | Node C | Q2 → VB | Pop Q2, write vertices, count → stopFlag
Single dispatch: vkCmdDispatch(96, 1, 1) = 96 WG × 32 threads = 3,072 persistent threads
Shader Main Loop Structure:
void main() {
uint wgId = gl_WorkGroupID.x;
uint localId = gl_LocalInvocationID.x;
// Node A: WG 0, Thread 0 seeds 3 edges (once)
if (wgId == 0 && localId == 0) {
if (atomicCompSwap(control.seedDone, 0, 1) == 0)
pushQ1(edge_AB); pushQ1(edge_BC); pushQ1(edge_CA);
}
barrier(); memoryBarrierBuffer();
// Main persistent loop
while (control.stopFlag == 0) {
if (wgId < NODE_C_START) { /* Node B */ }
else { /* Node C */ }
}
}
4 / 8

## Slide 5
Atomic Queue Mechanism
Ring Buffer Structure
QueueControl: head / tail / count
Task: payload[6] (4×float + depth + ready)
Push Protocol:
1. CAS count (reserve slot)
2. atomicAdd tail (get slot index)
3. Write payload[0–4]
4. memoryBarrierBuffer()
5. atomicExchange(ready, 1)
Pop Protocol:
1. CAS count (claim item)
2. atomicAdd head (get slot)
3. Spin: atomicCompSwap(ready,1,0)
4. Read payload
pushQ1() Implementation:
bool pushQ1(uint p0, uint p1, uint p2,
uint p3, uint p4) {
while (control.stopFlag == 0) {
uint cur = control.q1.count;
if (cur < QUEUE_SIZE) {
// CAS: reserve a slot
if (atomicCompSwap(control.q1.count,
cur, cur+1) == cur) {
uint slot = atomicAdd(
control.q1.tail, 1) % QUEUE_SIZE;
// Write payload
queue1.tasks[slot].payload[0] = p0;
queue1.tasks[slot].payload[1] = p1;
queue1.tasks[slot].payload[2] = p2;
queue1.tasks[slot].payload[3] = p3;
queue1.tasks[slot].payload[4] = p4;
memoryBarrierBuffer();
// Signal ready (atomic!)
atomicExchange(
queue1.tasks[slot].payload[5], 1u);
return true;
}
}
}
return false;
}
5 / 8

## Slide 6
Cross-Workgroup Memory Sync
Bug 1
Missing coherent modifier
Node C read stale count from L0/L1 cache → no task consumption
Fix: Added coherent to all SSBO declarations
Bug 2
Producer-consumer data race
Producer increments count then writes data; consumer reads uninitialized
Fix: Added per-slot payload[5] ready flag protocol
Bug 3
Plain store cross-CU unreliable
Plain store of ready flag not visible across CUs
Fix: All ready flags use atomicExchange / atomicCompSwap
Memory Visibility:
Method | Same WF | Same CU | Cross-CU
Plain load/store | ✔ | ~ | ✘
coherent | ✔ | ✔ | ~
Atomic (CAS/Exch) | ✔ | ✔ | ✔
6 / 8

## Slide 7
Koch Snowflake Algorithm
Subdivision Rule:
Each edge P1→P2 splits into 4 sub-edges:
P1 → A → C → B → P2
A, B = 1/3, 2/3 points along P1P2
C = apex point, rotated +60° from A
Growth: 3 × 4^depth edges
depth=4: 768 edges (1,536 vertices)
depth=6: 12,288 edges (24,576 vertices)
Node B: Subdivision Core:
// Koch subdivision: 1 edge -> 4 sub-edges
float dx = (x2 - x1) / 3.0;
float dy = (y2 - y1) / 3.0;
// A = 1/3 point, B = 2/3 point
float kax = x1 + dx, kay = y1 + dy;
float kbx = x1 + 2*dx, kby = y1 + 2*dy;
// C = apex (rotate +60° from A)
float cos60 = 0.5;
float sin60 = 0.8660254037844387;
float kcx = kax + dx*cos60 - dy*sin60;
float kcy = kay + dx*sin60 + dy*cos60;
// Push 4 sub-edges (depth+1)
pushQ1(P1→A); pushQ1(A→C);
pushQ1(C→B); pushQ1(B→P2);
GPU Self-Termination:
// Node C: auto-shutdown when all edges processed
uint processed = atomicAdd(control.totalProcessed, 1) + 1;
if (processed >= MAX_DEPTH_EDGES) {
atomicExchange(control.stopFlag, 1u); // all threads exit
}
Current Config (depth=6)
12,288 edges
24,576 vertices
7 / 8

## Slide 8
Progress & Next Steps
Completed
✔ Phase 1-2
Persistent threading, CAS-based queue, CPU monitoring
✔ Phase 3
Node A→B→C pipeline, feedback loop, workgroup roles
✔ Phase 4.1
GPU self-termination, per-frame compute+render, windowed display
Key Achievements:
• Cross-CU atomic sync validated on RDNA 3
• Zero CPU intervention (GPU self-scheduling)
• Single dispatch replaces multi-pass pipeline
• Koch snowflake: deterministic output verified
Next: Phase 4.2
GPU Timestamp Queries
vkCmdWriteTimestamp for compute timing measurement
CAS Failure Counters
Quantify atomic contention & scheduling overhead
LDS Queues
Intra-workgroup shared memory (10-100× latency reduction)
Subgroup Optimization
ballot/shuffle for RDNA3 occupancy tuning
8 / 8

## Slide 9
A Design Consideration: Pipeline Baseline
Current
Per-frame flow is fixed as GPU reset -> compute dispatch -> barrier -> render in one command buffer, with deterministic draw count.
Risk
This structure is excellent for bring-up and reproducibility, but it is not yet a performance-optimized scheduling design.
Next
Keep this as a correctness baseline; evaluate compute/graphics queue overlap and finer synchronization in a later optimization phase.
9 / 14

## Slide 10
A1 Termination Mechanism
Current
Node C increments totalProcessed and sets stopFlag when processed >= MAX_DEPTH_EDGES; termination is fully GPU-side.
Risk
Termination condition is count-driven. If parameters drift or workload changes, there is risk of early-stop or late-stop behavior.
Next
Move toward dual-condition termination (processed target + queue drain) while keeping no CPU polling in the hot path.
10 / 14

## Slide 11
A2 Role Mapping Strategy
Current
Roles are statically partitioned by workgroup ID: Node B for lower IDs and Node C for higher IDs (current split: 72/24 out of 96 WGs).
Risk
Fixed ratio may become imbalanced under different queue pressure patterns, causing waiting and unstable throughput.
Next
Treat NODE_C_START as a tuning parameter and later evaluate adaptive B/C ratio driven by runtime queue behavior.
11 / 14

## Slide 12
A3 Backing Memory and Queue Sizing
Current
Two fixed-size ring buffers (QUEUE_SIZE = 16384) are reset every frame and used for cross-workgroup producer-consumer handoff.
Risk
If queue capacity is too small, contention and long waits increase; if too large, memory footprint and locality pressure increase.
Next
Define a sizing rule from worst-case frontier growth plus margin, then validate with queue pressure instrumentation in a later step.
12 / 14

## Slide 13
A4 Memory Model and Atomic Cost
Current
Cross-workgroup shared states use atomic/CAS protocol (count/head/tail, ready flag, vertexCount, totalProcessed) with buffer barriers.
Risk
Correctness is protected, but global atomic hotspots can dominate scaling as concurrent workers contend on a small set of counters.
Next
Explore hierarchical or batched enqueue/dequeue patterns to reduce global contention after baseline behavior is fully characterized.
13 / 14

## Slide 14
A5 Spin Wait Risk (Identified, Not Measured Yet)
Current
Current queue push/pop and ready-flag handoff rely on busy-spin retries with atomic CAS; this is part of the correctness-first design.
Risk
Under producer-consumer imbalance, spin retries can grow and compress effective throughput; scalability may degrade before arithmetic saturation.
Next
For this report, we only flag the risk. Spin-cost quantification is intentionally out of scope and will be measured in a later phase.
14 / 14